## Slide 1: Comprehensive Country Ranking for Renewable Energy Based Mini-Grids Providing Rural Off-Grid Electrification
A.-K. Gerlach, E. Gaudchau, C. Cader, Ch. Breyer
2nd International Conference on Micro Perspectives
for Decentralized Energy Supply, 2013
Berlin, February 28, 2013

## Slide 2: Reiner Lemoine Institute
Scientific research for an energy transition towards 100% renewable energies
Reiner Lemoine
Founder of the Reiner Lemoine-Foundation
Research focuses:
Integrated energy systems
  Optimization of energy systems
  Energy transition processes
  Off-grid energy systems
RE-mobility
  Integration of renewable energies into mobility
Renewable energy technology
  Small wind power

## Slide 3
one energy generator,
one energy storage,
one control unit,
one consumer load and
at a capacity range of kW – MW
Mini-grids consist of at least
Mini-grids offer ideal conditions for a grid independent electricity supply.
Renewable Energy Mini-Grids

## Slide 4
Motivation for the Country Ranking
renewable energy based mini-grids are a key element for rural electrification
sustainable business models are needed for supplying hundreds of millions of people
comparison of all countries is a helpful indicator for players in the field

## Slide 5
Method for the Country Ranking
identification of main criteria and respective sub-criteria
  market potential
  political and financial environment
exclusion criteria
  electrification rates over 95 % and less than 200,000 people in rural areas without electricity
  high political instability
  very low diesel prices
weighting and scoring of each criterion
criteria not included
  no quantification possible
  not available on a global scale

## Slide 6: Consequences of Exclusion Criteria: Electrification
electrification rate > 95 % and
rural population without electricity < 200,000 people
 98 countries excluded

## Slide 7: Consequences of Exclusion Criteria: Travel Warning
travel warning
Afghanistan
Haiti
Iraq
Libya
Mali
Somalia
Syria
Yemen
travel warning by German Ministry of Foreign Affairs (April 2012):
partial travel warning
Algeria
Congo, DR
Georgia
Japan
Lebanon
Mauritania
Niger
Nigeria
Pakistan
West Bank

## Slide 8: Consequences of Exclusion Criteria: Political Stability
political stability (worldwide governance indicator) < 5th percentile
country | percentile rank
Somalia | 0,000
Pakistan | 0,472
Sudan | 0,943
Afghanistan | 1,415
Iraq | 1,887
Yemen | 2,358
Congo, DR | 2,830
Central African Republic | 3,302
Nigeria | 3,774
West Bank | 4,245
Guinea | 4,717
source: http://info.worldbank.org/governance/wgi/

## Slide 9: Consequences of Exclusion Criteria: Diesel Price
diesel price < 0.25 USD/ liter
country | pump price for diesel 2010 [USD/liter]
Venezuela | 0.01
Iran | 0.02
Saudi Arabia | 0.07
Bahrain | 0.13
Libya | 0.13
Algeria | 0.19
Qatar | 0.19
Turkmenistan | 0.20
Kuwait | 0.21
Yemen | 0.23
Brunei | 0.24
Motivation (roughly):
0.25 USD/l diesel price
0.19 €/l diesel price
0.019 €/kWhth diesel price
0.06 €/kWhel diesel-only

## Slide 10
A: market potential
    electrification rate [World Bank, IEA, UNDP]
    rural population without access to electricity [calculated]
    pump price for diesel fuel [World Bank]
B: political and financial environment
    political stability [World Bank]
    corruption perceptions index [Transparency Int]
    inflation [World Bank]
    ease of doing business index [World Bank]
50 %
30 %
15 %
20 %
15 %
50 %
20 %
40 %
60 %
comparative evaluation of target countries based on statistic data with regard to market potential plus political and financial environment
used criteria and and weighting factors:
Comparative Country Ranking: Criteria and Weighting

## Slide 11
  Good political and financial environment combined with high electrification needs are to be found especially in South and East Africa.
Results of the Country Ranking: All Criteria

## Slide 12
Results of the Country Ranking: Sub-Criteria
Market Potential
Political and Financial Environment
Key insight:
most top countries of market potential show low ranking for political and financial environment
and vice verca

## Slide 13: Results of the Country Ranking
rank | country | electrification rate [%] | rural population without access to electricity | worldwide governance indicators: political stability [%] | pump price for diesel fuel [USD/liter] | GDP per capita [USD]
1 | Rwanda | 5 | 8.5 mio | 41.5 | 1.62 | 530
2 | Zambia | 19 | 8.0 mio | 63.7 | 1.52 | 1,250
3 | South Africa | 75 | 8.6 mio | 44.3 | 1.14 | 7,280
4 | Botswana | 45 | 0.7 mio | 78.3 | 0.97 | 7,400
5 | Namibia | 34 | 1.2 mio | 71.7 | 1.09 | 5,330
6 | Ghana | 61 | 9.1 mio | 47.6 | 0.83 | 1,320
7 | Kenya | 16 | 29.9 mio | 13.7 | 1.27 | 790
8 | Uganda | 9 | 27.8 mio | 15.6 | 1.11 | 510
9 | United Republic of Tanzania | 14 | 32.3 mio | 45.8 | 1.19 | 520
10 | Peru | 86 | 5.9 mio | 20.3 | 1.10 | 5,400
top 10 countries:

## Slide 14
Rwanda – no 1 Country in the Ranking

## Slide 15
in general:
  large market size
  very good financial environment for foreign investors
energy sector:
  urgent needs to expand capacities, much imports, high tariffs
  target: 1,000 MW electric power capacity in 2017 (90 MW in 2011)
  investment in energy production with methane gas (large potential in lake Kivu), hydro power, geothermal and solar power
in terms of renewable based mini-grids:
  very low rural electrification rate
  independent power producer are allowed to work on- or off-grid
  “social tariffs need to be put in place to cater for the affordability of rural citizens”
focussing energy sector, rural electrification and investment possibilities
[pictures: Wikimedia Commons]
Rwanda – Summary Country Profile

## Slide 16: Summary
several countries offer good preconditions for RE-based mini-grids
top ranked countries are located in southern and eastern Africa
large market potential and poor political and financial environment are often coupled – and vice versa
countries have to be checked in detail for characteristics not included in the ranking

## Slide 17
Thanks for your attention.
… and in particular to SMA Stiftungsverbund gemeinnützige GmbH